Flow rate problems

(Poiseuille’s equation and Viscosity controlled flow)

Physics 202

For our purposes, Poiseuille’s equation relating pressure and fluid flow in pipes can be summarized as

(“Poiseuille’s equation”)

where r is the resistance of the pipe.

(In fairness to Poiseuille, we should point out that he also figured out that resistance is directly proportional to both viscosity (() and the length (l) of the pipe and it is inversely proportional to the fourth power of the radius of the pipe.   The exact relationship is:  )

Consider a horizontal section of pipe with water flowing from left to right.  There is a barrier producing resistance in the pipe.  The barrier has two holes in it (A and B) allowing water to flow through.  The situation is shown in the diagram below:

What can you say about the pressure(s) in region #1 and region #2?  How do you know?

What determines the flow rate through one of the holes (say, hole A)?  Is it the pressure itself or something special about the pressure?

The resistance of hole A turns out to be 3 (10 8 Pa s/m3.  The flow rate through hole A turns out to be 20 ml/s (2 ( 10-5 m3/s).  What does this tell you about the pressure around hole A?

Assuming the water isn’t moving very fast anywhere in the pipe and that the difference in height between the top and bottom of the pipe is very small, what can you say about the pressure around hole B?

The resistance of hole B turns out to be 6 (10 8 Pa s/m3.  What is the flow rate through hole B?

Now if we think of the entire barrier as a unit, with hole A and hole B as parts of the same thing, what is the flow rate through the barrier?

What is the resistance of the entire barrier (use Poiseuille’s equation).

How does the resistance of the entire barrier compare to the resistance of the individual holes?  Why?

Now imagine a similar section of pipe with two barriers in it.  Each barrier contains one hole exactly the same as the holes in the barrier from the previous problem. The situation is shown in the diagram below:

In order to make any progress, we have to assume that the wide regions of the pipe have so little resistance that it can be ignored.

There are two points labeled x and y within region #2.  If we are assuming that the resistance between these two points is zero, what does Poiseuille’s equation tell us about the pressure difference between these points?

Where in the diagram above could there be a pressure difference?  Where do you know the pressure must be the same?

The difference in pressure between region #1 and region #3 (call it (P13) turns out to be 18,000 Pa.  What does this tell you about the pressure difference between region #1 and region #2 (call it (P12) and the pressure difference between region #2 and region #3 (call it (P23)?

What must be the same at hole A and at hole B?  Could the flow rate be different in the two places?

Write an equation relating the flow rate through hole A to the pressure around point A.  Do the same for hole B.  Assuming the resistances are the same as in the last problem, how many unknowns do you have?

Can you come up with any more equations to help get rid of unknowns?

Find the flow rate through hole A and hole B.

Now consider the entire pipe as a unit.  Compare the pressure difference between the two ends of the pipe to the pressure difference across it.  What is the resistance of the entire pipe?

How does the resistance of the entire pipe compare to the resistance of the individual holes?  Why?